## Slide 1
Ignisia
THINK. BUILD. EVOLVE.
Track:
Theme:
Title:
Team ID:
INCUBEX
Prototype Expo Track
Aerospace & Space Technology / Hardware
AeroSync : Hybrid CanSat Telemetry & Launch Vehicle System
0007
Videos: https://drive.google.com/drive/folders/12sinTi2cqTp08u40LJMLwo98TNp7EeID

## Slide 2
Problem and limitations of existing solutions
⚡ WHY EXISTING SOLUTIONS FAIL — AND WHY WE BUILT SOMETHING BETTER
📡 DELAYED DATA
Delayed Data Recovery
Platforms require full recovery before data is accessible — zero real-time insight.
💰 PROHIBITIVE COST
Prohibitive Cost
Orbital infrastructure and satellite-grade hardware prices out student and research teams.
🔩 FRAGMENTED SENSING
Fragmented Sensing
Environmental, motion, and navigation data require separate, incompatible systems.
THE OPPORTUNITY
──────────────────
📍 Why It Matters
Altitude-based data powers weather forecasting, precision agriculture, disaster response and environmental monitoring — yet inaccessible without costly infrastructure.
🎯 Our Focus
Affordable, integrated sensing of environment, illumination, motion, and GPS in a single compact airborne platform.
COMPACT · AFFORDABLE · REAL-TIME
🛰 CUBESATS
Requires orbital launch infrastructure. High cost — inaccessible for rapid prototyping.
HIGH COST
🎈 WEATHER BALLOONS
Limited real-time telemetry. Data retrieved only after physical recovery of payload.
DELAYED DATA
🔬 LAB INSTRUMENTS
Stationary by design. Cannot capture altitude-varying atmospheric profiles in the field.
NO MOBILITY
📊 Altitude-based data is critical — yet no affordable, integrated, real-time solution existed. Until now.

## Slide 3
Our Solutions and it’s USP
Solution Description
Features & USP
The Teensy 4.1 collects, timestamps, and validates environmental, illumination, motion, and GPS data before transmitting telemetry to the ground station via 433 MHz LoRa
REAL-TIME TELEMETRY
433 MHz LoRa transmits live sensor, GPS, and motion data to the ground station.
GPS NAVIGATION
NEO-6M provides position, altitude, speed, satellite count, and HDOP.
🌡️ MULTI-DOMAIN SENSING
Measures pressure, temperature, humidity, illumination, and 9-DOF motion.
CROSS-VALIDATION
BME280 and SHT31 cross-check temperature and humidity readings.

## Slide 4
Technical Architecture
Tech Stack
System Architecture Diagram
FLIGHT HARDWARE
Teensy 4.1 | 600 MHz ARM M7 flight computer
BME280 | Pressure, temperature, humidity
SHT31 | Independent precision temp + humidity cross-check channel
VEML6030 | Ambient illumination sensing
LSM9DS1 | 9-DOF accelerometer, gyroscope, magnetometer
NEO-6M GPS | Position, altitude, speed, HDOP
COMMUNICATION & SOFTWARE
AS32-TTL-100 | 433 MHz LoRa radio; airborne long-range transmitter
E32-433T30D | Ground-side 433 MHz LoRa receiver module
C++ / Arduino | Embedded firmware language and real-time environment
TinyGPS++ | Lightweight NMEA stream parser for navigation data
Mission Planner | ArduPilot telemetry display & drone mission mapping
Compact · Modular · Real-Time · Multi-Domain | Sensors → Teensy 4.1 → 433 MHz LoRa → Ground Station Live Dashboard

## Slide 5
Working of the Solution and Demonstration
Methodology
CanSat Images
Charts
🚀 LAUNCH & EJECTION
🌡️ SENSE & PROCESS
📡 TRANSMIT — 433 MHz
🖥️ GROUND DISPLAY
CanSat ejected from carrier vehicle; mission timer starts
9 sensors sampled; Teensy 4.1 encodes telemetry packets
LoRa radio broadcasts structured packets every cycle
Ground station decodes, logs, plots and maps live data
POWER ON
Sensors initialize; GPS acquires 3D fix; hardware health check passes.
LAUNCH
CanSat ejected from carrier at apogee; mission timer begins automatically.
DESCENT
Parachute deploys; continuous descent telemetry; GPS tracks location.
LANDING
Final landing GPS fix and battery status sent; mission elapsed time logged.
CanSat Payload —+ LoRa TX + GPS + BatteryTeensy 4.1 + 5 Sensors
ALTITUDE PROFILE — CanSat Mission (Simulated Telemetry)
Chart: 
| 0s | 10s | 20s | 30s | 40s | 50s | 60s | 70s | 80s | 90s | 100s | 110s | 120s
 | 0 | 45 | 120 | 185 | 200 | 195 | 172 | 150 | 124 | 97 | 68 | 38 | 3
TEMPERATURE PROFILE — Descent Phase
Chart: 
| 0s | 10s | 20s | 30s | 40s | 50s | 60s | 70s | 80s | 90s | 100s | 110s | 120s
 | 28.2 | 27.5 | 26.1 | 24.7 | 23.3 | 23.5 | 24.4 | 25.1 | 25.8 | 26.4 | 27 | 27.6 | 28.1
9 Params Logged in sync
~2 s Packet interval
>95% Packet delivery
Live Ground Station — Real-time telemetry decoded and displayed

## Slide 6
Impact and Benefits
Social / Environmental / Governmental
How solution addresses the problem
Environmental Monitoring
Real-time atmospheric data supports microclimate analysis, climate research, and environmental monitoring.
Precision Agriculture
Altitude-based sensing helps study crop microclimates, temperature variations, and heat stress.
Disaster Response
GPS-tracked telemetry supports aerial reconnaissance and atmospheric monitoring during extreme events.
Accessible Aerospace
Affordable, modular hardware gives students hands-on experience in aerospace engineering and telemetry.
Real-Time Telemetry
• 433 MHz LoRa link transmits live altitude, temperature, humidity, GPS, and motion data no post-recovery wait.
Multi-Sensor Environmental Sensing
• BME280 + SHT31 + VEML6030 + LSM9DS1 provide cross-validated atmospheric, illumination, and motion data.
GPS Navigation & Tracking
• u-blox NEO-6M provides real-time position, altitude, speed, and satellite count — enabling aerial tracking.
Aerial Sensors
BME280 · SHT31 · VEML6030 LSM9DS1 · u-blox GPS
Teensy 4.1
Real-time processing, timestamps & validation
433 MHz LoRa
AS32-TTL-100 long-range airborne radio broadcast
Ground Station
Live telemetry dashboard, GPS track & CSV logging
Intelligence
Localized atmospheric data, heat stress & hazard analysis
CanSat → Atmospheric Data → Real-Time Telemetry → Environmental & Disaster Intelligence

## Slide 7
Future Plan and Feasibilty
Challenges and Mitigation
Economic Viability and Commercialisation Scalability
Future Scope
CHALLENGES & RISKS
MITIGATION STRATEGIES
GPS Signal Loss
• Temporary loss of GPS positioning.
• Flag invalid GPS data; continue sensor and IMU telemetry.
Radio Link Interruption
• 433 MHz signal dropouts or interference.
• Packet counters identify losses; transmission resumes after reconnection.
Power & Sensor Reliability
• Voltage drops or sensor faults.
•Log battery voltage; cross-check temperature and humidity readings.
Low-Cost Modular Platform
Teensy 4.1 and off-the-shelf sensors. Build cost under ₹8,000.
Scalable & Extensible Architecture
Modular I²C/UART interfaces enable additional sensors and dashboards.
Commercialisation & Deployment Path
Potential applications in agriculture, weather monitoring, and disaster response.
Web Ground Dashboard
Autonomous Event Detection
Sensor Fusion & Estimation
Drone Payload Integration

## Slide 8
Research and References
[1] Design of Trash Can Sized Satellite for Air Quality Monitoring at an Altitude of 300m Above Ground Level. Summary: Presents a compact CanSat designed to monitor air quality at 300 m altitude, using LoRa telemetry, a parachute-based descent system, and a ground station for receiving sensor data. Highly relevant to CanSat hardware and communication architecture..
Link: https://ieeexplore.ieee.org/document/10245113/
[2] Swayampakula et al., “Design and development of a CanSat for air pollution monitoring with RSSI based position retrieval system,” Advances in Space Research, Vol. 75, Issue 9, 2025. Summary: Describes a lightweight CanSat for atmospheric and air-pollution monitoring using temperature, humidity, and gas sensors. Covers telemetry, position retrieval using received signal strength (RSSI), power conservation, and parachute-based descent.Link: https://www.sciencedirect.com/science/article/pii/S0273117724001856?via%3Dihub
[3] N. Sako et al., “CanSat suborbital launch experiment—university educational space program using can sized pico-satellite,” Acta Astronautica, Vol. 48, Issues 5–12, pp. 767–776, 2001.. Summary: Presents the design, objectives, suborbital launch experiments, and lessons learned from a can-sized pico-satellite project. Useful for explaining CanSat mission design, deployment, and experimental validation. Link: https://linkinghub.elsevier.com/retrieve/pii/S009457650100039X
[4] “A pico-satellite assembled and tested during the 6th CanSat Leader Training Program,” Journal of Applied Research and Technology, Vol. 15, Issue 1, pp. 83–91, 2017. Summary: Describes the construction and testing of a small satellite carrying temperature and humidity sensors. Includes GPS-based position data and atmospheric measurements during flight, making it useful for sensor integration and experimental testing.
Link: https://doi.org/10.1016/j.jart.2016.10.003
Videos: https://drive.google.com/drive/folders/12sinTi2cqTp08u40LJMLwo98TNp7EeID